CONTENTS

Product Features and Specifications ..............................................1

Installation Requirement .............................................................3

Steps of Installation ………………………………………………..…………………………….4

Exploded View ...........................................................................24

Test Run ................................................................................. .28

Operation Instruction .................................................................29

Maintenance .............................................................................30

Trouble Shooting .......................................................................31

Parts List .................................................................................32

I. PRODUCT FEATURES AND SPECIFICATIONS

CLEAR-FLOOR DIRECT-DRIVED MODEL FEATURES

Model 209C 209CH (See Fig. 1)

· Direct-drived design, minimize the lift wear parts and breakdown ratio

· Dual hydraulic cylinders, designed and made on ANSI standards, utilizing NOK oil seal in cylinder

· Self- lubricating UHMW Polyethylene sliders and bronze bush

· Single-point safety release, and dual safety design

. Clear-floor design, provide unobstructed floor use

. Overhead safety shut-off device prevents vehicle damage

· Super-symmetric arms design, stackable rubber pads

. Standard adjustable heights accommodates varying ceiling heights

MODEL 209C 209CH SPECIFICATIONS

| Model | Style | Lifting Capacity | Lifting Time | Lifting Height | Overall Height | Overall Width | Width Between Columns | Minimum Pad Height | Motor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 209C | Clear-floor Direct-drived | 4.0T 9,000 lbs | 52S | 1815-2044mm 71 1/2”–80 1/2” | 3621/3821mm 142 1/2”/ 150 1/2” | 3428mm 135” | 2850mm 112 1/4” | 90mm 3 1/2” | 2.0/3.0 HP |
| 209CH | Clear-floor Direct-drived | 4.0T 9,000 lbs | 52S | 1815-2044mm 71 1/2”–80 1/2” | 4231/4431 mm 166 1/2” /174 1/2” | 3428mm 135” | 2850mm 112 1/4” | 90mm 3 1/2” | 2.0/3.0 HP |

Arm Swings View

For Model 209C  209CH

II. INSTALLATION REQUIREMENT

TOOLS REQUIRED

  - Rotary Hammer Drill (Φ19)

  - Hammer

  - Level Bar

  - English Spanner (12")

  - Ratchet Spanner With Socket (28#)

( Wrench set

(8#, 10#, 13#, 14#, 17#, 19#, 24#)

  - Carpenter’s Chalk

  - Screw Sets

  - Tape Measure (7.5m)

  - Pliers

  - Socket Head Wrench (3#, 5#, 8#)

(  Lock Wrench

Fig. 3

B. SPECIFICATIONS OF CONCRETE (See Fig. 4)

Specifications of concrete must be adhered to the specification as following.

Failure to do so may result in lift and/or vehicle falling.

1. Concrete must be thickness 100mm minimum and without reinforcing steel bars, and must be dried completely before the installation.

2. Concrete must be in good condition and must be of test strength 3,000psi (210kg/cm²) minimum.

3. Floors must be level and no cracks.

C. POWER SUPPLY

The electrical source must be 2.2kw minimum. The source cable size must be 2.5mm² and in good condition of contacting with floor.

III. STEPS OF INSTALLATION

A. Location of Installation

Check and insure the installation location (concrete, layout, space size etc.) is        suitable for lift installation.

B. Use a carpenter’s chalk line to establish installation layout of baseplate (See Fig.5).

C. Check the parts before assembly.

1. Packaged lift and hydraulic power unit (See Fig. 6).

2. Move aside the lift with fork lift or hoist, and open the extension packing carefully , take off the lifting arms and parts box from upper and inside the column, then move them to location nearby installation site, check the parts according to the shipment parts list (See Fig.7).

3. Loose the screws of the upper package stand, take off the upper extension columns, take out the parts in the inner column and remove the package stand

4. Move aside the parts and check the parts according to the shipment parts list

(See Fig.8, 9).

5. Open the bag 1 of parts and check the parts according to parts box list (See Fig. 10).

6. Open the bag 2 of parts and check the parts according to parts bag list (See Fig. 11).

D. Install parts of extension columns (See Fig. 12).

E. Position powerside column

Lay down two columns on the installation site parallelly, position the powerside column according to the actual installation site. Usually, it is suggested to install powerside column on the front-right side from which vehicles are driven to the lift. This lift is designed with 2-Section columns. Adjustable height according to the ceiling height and connecting the inner and extension columns.

1. When the ceiling height is less than 3850mm (151 1/2”) for 209C, 4460mm (175 5/8”) for 209CH, connecting the extension columns with the upper hole (See Fig.13).

2. When the ceiling height is over 3850mm (151 1/2”) for 209C, 4460mm (175 5/8”) for 209CH, connecting the extension columns with the lower hole (See Fig.14).

F. Position columns (See Fig. 15)

Position the columns on the installation layout of baseplate, Install the anchor bolts. Check the Columns plumbness with level bar, and adjusting with the shims if the columns are not vertical. Do not tighten the Anchor Bolts.

G. Install overhead top beam

1. With help of the hook of top beam, put one side of top beam on top of the extension column and connecting the top beam to extension column by bolts, tighten the bolts. Then assemble the connecting bracket (See Fig. 16).

2. Assemble overhead top beam, tighten the columns anchor bolts (See Fig. 17).

H. Installing the limit switch control bar and limit switch (See Fig. 18).

I. Install safety device (See Fig. 19 & Fig. 20).

J. Lift the carriages up to about one meter high by hand and make them be locked at the same level (See Fig. 21).

K. Install cables

1. Low setting cable connection (See Fig. 22).

2．High setting cable connection

2.1. Cable pass through from the bottom of the carriages and be pulled out from the

open of carriages, then screw the two cable nuts (See Fig. 23).

2.2 Connecting cable for high setting (See Fig. 24).

L. Install hydraulic power unit and oil hose assy. (See Fig. 25).

Tighten all the hydraulic fittings, and fill the reservoir with hydraulic oil.

Note: In consideration of Hydraulic Power Unit’s durability and keep the equipment running in the perfect condition, please use Hydraulic Oil 46#.

M. Install safety cable (See Fig. 26)

N. Oil Hose & Protective Covers

1. Install Oil Hose.

Note: Don’t cross the oil hose and safety cable together (See Fig. 27 & Fig. 28).

2. Install safety cable, oil hose and protective cover (See Fig. 29 & Fig. 30 & Fig. 31).

Note: Install the protective cover on the extension column with M6*35 cup head bolt, Install the protective cover on the inner column with M6*40 cup head bolt.

O. Install lifting arms and adjust the arm locks.

1. Install the lifting arms (See Fig. 32).

2. Lowing the carriages down to the lowest position, then use the 8# socket head wrench to loosen the socket bolt (See Fig. 33).

3. Adjust the arm lock as direction of arrow (See Fig. 34)

4. Adjust moon gear and arm lock to make it to be meshed, then tighten the socket bolts of arm lock (See Fig. 35).

P. Install electrical system

Connect the power source on the data plate of power unit.

Note: 1. For the safety of operators, the power wiring must contact the floor well.

2. Pay attention to the direction of rotations when using three phase motors.

PEAK single phase motor (See Fig. 36).

- Connecting the two power supply wires (active wire L and neutral wire N) to terminals of AC contactor marked L1, L2 respectively.

- Connecting the two motor wires to terminals of AC contactor marked T1, T2.

- Connecting A2 to L2 of AC contactor.

- Connecting the limit switch: Removing the wire of connecting terminal 4# of control button and A1 of AC contactor firstly (See Fig. 37), then connecting wire12#(brown wire) of limit switch with terminal 4# of control button and connecting wire 11#(blue wire) with terminals A1 of AC contactor respectively. Connecting the earth wire of limit switch to the earth wire terminal on the motor. (See Fig. 38).

- Terminal 3# on the control button is connected with terminal L1 on the AC contactor.

SPX single phase motor (See Fig. 39)

- Power supply wire (neutral wire N) is connected with wire 5# of motor.

- Wire 11# (blue wire) of limit switch is connected with wire 6# of the motor.

- Wire 12#(Brown wire) of limit switch is connected with wire 4# of control button.

- Earth wire( yellow and green wire) of limit switch is connected with the earth wire terminal on the motor.

- Power supply wire (active wire L) is connected with wire 3# of control button.

Three phase motor

1. Circuit diagram (See Fig. 40)

- Connection step (See Fig. 41)

a. The source wires (L1, L2, L3) are connected with terminals of AC contactor marked L1, L2, L3 respectively.

b. Terminals 4# of control button is connected with wire 12#（brown wire） of limit switch; wire 11#(blue wire) is connected with A1 terminal of AC contactor, Earth wire( yellow and green wire) of limit switch is connected with the earth wire  terminal of the motor.

C. Terminals 3# of control button is connected with L1 terminals of AC contactor.

IV. EXPLODED VIEW

Model 209C  209CH

Cylinders

Fig. 43

SPX MANUAL POWER UNIT, 220V/50Hz, Single phase

PEAK MANUAL POWER UNIT

Illustration of hydraulic valve for SPX & PEAK hydraulic power unit

a. SPX manual power unit, 220V/50HZ, Single phase (See Fig. 46)

b. PEAK manual power unit, 220V/50HZ, Single phase (See Fig. 47)

C. PEAK manual power unit, 380V/50HZ, 3 phase (See Fig. 48)

V. TEST RUN

1. Adjust synchronous cable (See Fig. 49)

Use wrench to hold the cable fitting, meanwhile

use ratchet spanner to tighten the cable nut.

Make sure two cables are with the same tension

so that two carriage can work synchronously.

Fit the plastic hole cover on the lifting head.

If the carriage does not Synchronize when lifting,

please tighten the cable nut of lower side carriage.

2. Adjust Safety Cable

Lifting the carriage and lock at the same height, strain the safety cable and then release a little, and then tighten the cable nuts. Make sure the safety device can always be worked properly.

3. Bleeding air

This hydraulic system is designed to bleeding air by loosing

the bleeding plug. Lifting the carriages to about 1 meter

height, and loose the bleeding plug, the air would be

bled automatically, then tighten the plug after bleeding,

the lift would work stably and smoothly,

otherwise repeat bleeding (See Fig. 50).

4. Adjust the lower speed (Only for PEAK power unit)

You can adjust the lower speed of the lift if needing: Loosen the fixing nut of the throttle valve, and then turn the throttle valve clockwise to decrease the lower speed, or counterclockwise to increase the lower speed. Do not forget to tighten the fixing nut after the lower speed adjustment has been done.

5. Test with load

After finishing the above adjustment, test running the lift with load. Run the lift in low position for several times first, make sure the lift can rise and lower synchronously,  the Safety Device can lock and release synchronously. And then test run the lift to the top completely. If there are anything improper, repeat the above adjustment.

NOTE: It may be vibrated when lifting at start, please lifting it with load for several times, the air would be bled and the vibration would be disappeared automatically.

Fig. 52  Hydraulic System

VI. OPERATION INSTRUCTIONS

Please read the safety tips carefully before operating the lift

To lift vehicle

- Keep clean of site near the lift;

- Position lift arms to the lowest position;

- To shortest lift arms;

- Open lift arms;

- Position vehicle between columns;

- Move arms to the vehicle’s lifting point;

Note: The four lift arms must at the same time contact the vehicle’s lifting point where manufacturers recommended

- Push button ”UP” until the lift pads contact underside of vehicle totally. Recheck to make sure vehicle is secure;

- Continue to raise the lift slowly to the desired working height, ensuring the balance of vehicle;

- Push lowering handle to lower lift onto the nearest safety. The vehicle is ready to repair.

To lower vehicle

- Be sure clear of around and under the lift, only leaving operator in lift area;

- Push button ”UP” to raise the vehicle slightly, and then release the safety device, lower vehicle by pushing lowering handle.

- Open the arms and position them to the shortest length;

- Drive away the vehicle.

- Turn off the power.

VII.MAINTENANCE SCHEDULE

Monthly:

- Re-torque the anchor bolts to 150 Nm;

- Check all connectors, bolts and pins to insure proper mounting;

- Lubricate cable with lubricant;

- Make a visual inspection of all hydraulic hoses/lines for possible wear or leakage;

- Check Safety device and make sure proper condition;

- Lubricate all Rollers and Pins with 90wt. Gear oil or equivalent;

Note: All anchor bolts should take full torque. If any of the bolts does not function for any reason, DO NOT use the lift until the bolt has been replaced.

Every six months:

- Make a visual inspection of all moving parts for possible wear, interference or damage.

- Check and adjust as necessary, equalizer tension of the cables to insure level lifting.

- Check columns for plumbness.

- Check Rubber Pads and replace as necessary.

- Check Safety device and make sure proper condition.

VIII.TROUBLE SHOOTING

| TROUBLE | CAUSE | REMEDY |
| --- | --- | --- |
| Motor does not run | 1. Button does not work 2. Wiring connections are not in good condition 3. Motor burned out 4. Height Limit Switch is damaged 5. AC contactor burned out | 1. Replace button 2.Repair all wiring connections 3. Repair or replace motor 4.Replace the Limit Switch 5. Replace AC Contactor |
| Motor runs but the lift is not raised | 1. Motor runs in reverse rotation 2. Gear Pump out of operation 3. Release Valve in damage 4. Relief Valve or Check Valve in damage 5. Low oil level | 1.Reverse two power wire 2.Repair or replace 3. Repair or replace 4.Repair or replace 5.Fill tank |
| Lift does not stay up | 1. Release Valve out of work 2. Relief Valve or Check Valve leakage 3. Cylinder or Fittings leaks | Repair or replace |
| Lift raises slowly | 1. Oil line is jammed 2. Motor running on low voltage 3. Oil mixed with air 4. Gear Pump leaks 5. Overload lifting | 1. Clean the oil line 2. Check Electrical System 3. Fill tank 4. Replace Pump 5. Check load |
| Lift cannot lower | 1. Safety device are in activated 2. Release Valve in damage 3. Safety cable broken 4. Oil system is jammed | 1. Release the safeties 2. Repair or replace 3. Replace 4. Clean the oil system |

IX. PARTS LIST FOR 209C and 209CH (See Fig. 42, Fig. 4)

| Item | Part# | Description | Qty. | Note |
| --- | --- | --- | --- | --- |
|  |  |  | 209C | 209CH |  |
| 1 | 206019 | Snap Ring | 6 | 6 |  |
| 2 | 206058 | Screw | 2 | 2 |  |
| 3 | 206059 | Washer | 2 | 2 |  |
| 4 | 209057B | Bronze Bush For Pulley | 6 | 6 |  |
| 5 | 206020 | Pulley | 6 | 6 |  |
| 6 | 206001C | Powerside Inner Column | 1 | 1 |  |
| 201 | 209002 | Manual Power Unit | 1 | 1 |  |
| 7 | 209003 | Hex Bolt | 8 | 8 |  |
| 8 | 209004 | Rubber Ring | 4 | 4 |  |
| 9 | 209005 | Self locking Nut | 8 | 8 |  |
| 10 | 206002 | Safety Pin | 2 | 2 |  |
| 11 | 209007A | Safety Spring | 2 | 2 |  |
| 12 | 206003 | Handle Protective Plastic cushion | 1 | 1 |  |
| 13 | 206004 | Powerside Safety Lock | 1 | 1 |  |
| 14 | 209012 | Hair Pin | 2 | 2 |  |
| 15 | 206006 | Washer | 22 | 22 |  |
| 16 | 206023A | Hex Nut | 2 | 2 |  |
| 17 | 209009 | Cup Head Bolt | 10 | 10 |  |
| 18 | 206004A | Safety Pulley Bracket | 1 | 1 |  |
| 19 | 206081 | Safety Cover | 2 | 2 |  |
| 20 | 206017 | Hex Bolt | 10 | 10 |  |
| 21 | 209022 | Washer | 52 | 52 |  |
| 22 | 209021 | Hex Nut | 20 | 20 |  |
| 23 | 206010 | Safety Pulley Bracket | 1 | 1 |  |
| 24 | 206009 | Plastic Pulley | 5 | 5 |  |
| 25 | 209010 | Snap Ring | 5 | 5 |  |
| 26 | 209033 | Washer | 18 | 18 |  |
| 27 | 206151 | Extension Column | 2 | 0 |  |
|  | 206152 |  | 0 | 2 |  |
| 28 | 206137 | Wire Cable | 1 | 0 |  |
|  | 206138 |  | 0 | 1 |  |
| 29 | 209111 | Protective Ring For Cylinder | 2 | 2 |  |
| 30 | 217056 | Hydraulic Cylinder | 2 | 2 |  |
| 31 | 209015 | Slider Block | 16 | 16 |  |
| 32 | 206046A | Arm Lock Bar (left) | 2 | 2 |  |
| 33 | 206050A | Spring | 4 | 4 |  |
| 34 | 217044 | Arm Lock | 4 | 4 |  |
| 35 | 206032 | Snap Ring | 4 | 4 |  |

| Item | Part# | Description | Qty. | Note |
| --- | --- | --- | --- | --- |
|  |  |  | 209C | 209CH |  |
| 36 | 206036 | Hair Pin | 4 | 4 |  |
| 37 | 209016 | Carriage Plastic Cover | 2 | 2 |  |
| 38 | 206046B | Arm Lock Bar (right) | 2 | 2 |  |
| 39 | 206136 | Arm Pin | 4 | 4 |  |
| 39A | 520023 | Snap Ring | 4 | 4 |  |
| 40 | 206048 | Socket Bolt | 12 | 12 |  |
| 41 | 206049 | Moon Gear | 4 | 4 |  |
| 42 | 209019 | Screw | 12 | 12 |  |
| 43 | 209018 | Protective Rubber | 2 | 2 |  |
| 44 | 206111A | Carriage | 2 | 2 |  |
| 45 | 206167 | Lifting Arm - Front (drop-in) | 2 | 2 |  |
| 45A | 206173 | Extended Arm - Front | 2 | 2 |  |
| 45B | 206174 | Middle Arm - Front | 2 | 2 |  |
| 45C | 206089A | Inner Arm - Front | 2 | 2 |  |
| 46 | 206168 | Lifting Arm - Rear (drop-in) | 2 | 2 |  |
| 46A | 206175 | Extended Arm - Rear | 2 | 2 |  |
| 46B | 206176 | Inner Arm - Rear | 2 | 2 |  |
| 47 | 209034 | Lock washer | 12 | 12 |  |
| 48 | 209039 | Lock washer | 32 | 32 |  |
| 49 | 201046A | Rubber Pad Assy. | 4 | 4 |  |
| 49A | 420138 | Socket bolt | 4 | 4 |  |
| 49B | 209134 | Rubber Pad | 4 | 4 |  |
| 49C | 680030C | Rubber Pad Frame | 4 | 4 |  |
| 50 | 209126 | Hex Bolt | 20 | 20 |  |
| 51 | 201002 | Hex Bolt | 14 | 14 |  |
| 52 | 206025A | Foam Cushion | 1 | 1 |  |
| 53 | 201005 | Split Pin | 2 | 2 |  |
| 54 | 206129 | Control Bar | 1 | 1 |  |
| 55 | 206025C | Connecting Pin for Control Bar | 2 | 2 |  |
| 56 | 206013 | Limit Switch | 1 | 1 |  |
| 57 | 206011 | Cup Head Bolt | 2 | 2 |  |
| 58 | 206042 | Control Bar Support Bracket | 2 | 2 |  |
| 59 | 206041 | Hex Bolt | 4 | 4 |  |
| 60 | 206023 | Self locking Nut | 12 | 12 |  |
| 61 | 209056 | Self locking Nut | 10 | 10 |  |
| 62 | 206016 | Connecting Bracket | 1 | 1 |  |
| 63 | 206018B | Top Beam W/Bracket | 2 | 2 |  |
| 64 | 206028 | Cup Head Bolt | 4 | 4 |  |
| 65 | 206029 | Retainer | 2 | 2 |  |
| Item | Part# | Description | Qty. | Note |
|  |  |  | 209C | 209CH |  |
| 66 | 206021 | Pin For Pulley | 2 | 2 |  |
| 67 | 206022 | Top Pulley Tube | 2 | 2 |  |
| 68 | 206024 | Hex Bolt | 8 | 8 |  |
| 69 | 206010A | Safety Pulley Bracket | 1 | 1 |  |
| 70 | 206085 | Protective Cover(L=1240mm) | 2 | 0 |  |
|  | 206086 | Protective Cover(L=1850mm) | 0 | 2 |  |
| 71 | 206084 | Protective Cover(L=200mm) | 2 | 2 |  |
| 72 | 206083 | Protective Cover(L=385mm) | 2 | 2 |  |
| 73 | 640050 | Socket bolt | 4 | 4 |  |
| 74 | 206008C | Safety Pulley Bracket | 1 | 1 |  |
| 75 | 206026A | Offside Safety Lock | 1 | 1 |  |
| 76 | 206080 | Protective Cover(L=1565mm) | 2 | 2 |  |
| 77 | 206079 | Cup Head Bolt | 14 | 14 |  |
| 77A | 206110 | Cup Head Bolt | 6 | 6 |  |
| 78 | 206030C | Offside Inner column | 1 | 1 |  |
| 79 | 209051B | Stackable Adapter (1.5”) | 4 | 4 |  |
| 80 | 209052B | Stackable Adapter (2.5”) | 4 | 4 |  |
| 81 | 209053B | Stackable Adapter (5”) | 4 | 4 |  |
| 82 | 209059B | Anchor Bolt | 10 | 10 |  |
| 83 | 217048 | Retainer | 2 | 2 |  |
| 84 | 209066 | Hex Nut | 8 | 8 |  |
| 84A | 620065 | Shim(2mm) | 10 | 10 |  |
| 84B | 201090 | Shim (1mm) | 10 | 10 |  |
| 84C | 206155 | Front toe guard | 2 | 2 |  |
| 84D | 206154 | Rear toe guard | 2 | 2 |  |
| 84E | 206156 | Tool tray | 2 | 2 |  |
| Parts For Oil Hose, Fitting & Cable (See Fig. 24-26) |
| 85 | 206064A | Cable | 2 | 0 |  |
|  | 206064B | Cable | 0 | 2 |  |
| 86 | 206132 | Oil hose | 1 | 0 |  |
|  | 206133 |  | 0 | 1 |  |
| 87 | 209060 | 90°Fitting For Hydraulic Power Unit | 1 | 1 |  |
| 87A | 211016 | T fitting | 1 | 1 |  |
| 88 | 209064 | Straight Fitting | 2 | 2 |  |
| 89 | 206062 | Straight Fitting | 2 | 2 |  |
| 90 | 233009 | Pipe Fitting | 2 | 2 |  |
| 91 | 206130 | Oil Hose | 2 | 0 |  |
|  | 206131 |  | 0 | 2 |  |

| Item | Part# | Description | Qty. | Note |
| --- | --- | --- | --- | --- |
|  |  |  | 209C | 209CH |  |
| 92 | 260149 | Safety cable | 1 | 0 |  |
|  | 206065A |  | 0 | 1 |  |
| 93 | 420045 | Washer | 14 | 14 |  |
| 94 | 209149 | Lock washer | 4 | 4 |  |
| 95 | 209152 | Ties | 4 | 4 |  |
| 96 | 206500B | Parts Box | 1 | 0 |  |
|  | 206501B |  | 0 | 1 |  |
| Parts for hydraulic cylinder (See Fig.43) |
| 30-1 | 209069 | O-Ring | 2 | 2 |  |
| 30-2 | 209070 | Bleeding Plug | 2 | 2 |  |
| 30-3 | 209071 | Support Ring | 2 | 2 |  |
| 30-4 | 209072 | Y-Ring | 2 | 2 |  |
| 30-5 | 209073 | O-Ring | 2 | 2 |  |
| 30-6 | 209074 | Piston | 2 | 2 |  |
| 30-7 | 209075 | O-Ring | 2 | 2 |  |
| 30-8 | 217076 | Piston Rod | 2 | 2 |  |
| 30-9 | 209077 | Piston Rod Fitting | 2 | 2 |  |
| 30-10 | 209078 | Dust Ring | 2 | 2 |  |
| 30-11 | 209079 | Head Cap | 2 | 2 |  |
| 30-12 | 209080 | O-Ring | 2 | 2 |  |
| 30-13 | 209081A | Bore Weldment | 2 | 2 |  |
| Parts For SPX Manual Power Unit, 220V/50Hz/1 phase (See Fig. 44) |
| 201-1 | 81400030 | Motor | 1 | 1 |  |
| 201-2 | 81400159 | Protective Ring | 1 | 1 |  |
| 201-3 | 81400063 | Motor Connecting Shaft | 1 | 1 |  |
| 201-4 | 81400031 | Valve Body | 1 | 1 |  |
| 201-5 | 81400160 | Relief Valve | 1 | 1 |  |
| 201-6 | 81400161 | Lock Washer | 4 | 4 |  |
| 201-7 | 81400162 | Socket Bolt | 4 | 4 |  |
| 201-8 | 81400121 | Inlet Pipe | 1 | 1 |  |
| 201-9 | 81400163 | O-Ring | 1 | 1 |  |
| 201-10 | 81400164 | Filter | 1 | 1 |  |
| 201-11 | 81400165 | Hex bolt | 4 | 4 |  |
| 201-12 | 81400093 | Reservoir | 1 | 1 |  |
| 201-13 | 81400166 | Head Screw | 2 | 2 |  |
| 201-14 | 81400167 | Cover of Capacitor | 1 | 1 |  |
| 201-15 | 81400087 | Capacitor | 1 | 1 |  |
| 201-16 | 81400168 | Rubber Gasket | 1 | 1 |  |
| 201-17 | 81400169 | Hex bolt | 1 | 1 |  |
| 201-18 | 81400062 | Cover of Motor Terminal Box | 1 | 1 |  |
| 201-19 | 81400028 | Push Button | 1 | 1 |  |

| Item | Part# | Description | Qty. | Note |
| --- | --- | --- | --- | --- |
|  |  |  | 209C | 209CH |  |
| 201-20 | 81400105 | Release Valve | 1 | 1 |  |
| 201-21 | 81400033 | Handle For Release Valve | 1 | 1 |  |
| 201-22 | 81400170 | Washer | 1 | 1 |  |
| 201-23 | 81400171 | Hex Nut | 1 | 1 |  |
| 201-24 | 81400043 | Check Valve | 1 | 1 |  |
| 201-25 | 81400123 | Gear Pump | 1 | 1 |  |
| 201-26 | 81400122 | Oil Return Pipe | 1 | 1 |  |
| 201-27 | 81400172 | Filer Cap | 1 | 1 |  |
| Parts For PEAK Manual Power Unit, 220V/50Hz/1phase (See Fig. 45) |
| 201A-1 | 81400048 | Motor | 1 | 1 |  |
| 201A-2 | 81400178 | Protective Ring | 1 | 1 |  |
| 201A-3 | 81400179 | AC contactor | 1 | 1 |  |
| 201A-4 | 81400127 | Motor Connecting Shaft | 1 | 1 |  |
| 201A-5 | 81400067 | Valve Body | 1 | 1 |  |
| 201A-6 | 81400106 | Relief Valve | 1 | 1 |  |
| 201A-7 | 81400107 | Throttle valve | 1 | 1 |  |
| 201A-8 | 209149 | Lock Washer | 4 | 4 |  |
| 201A-9 | 81400148 | Socket Bolt | 4 | 4 |  |
| 201A-10 | 81400134 | Inlet Pipe | 1 | 1 |  |
| 201A-11 | 81400144 | O-Ring | 1 | 1 |  |
| 201A-12 | 81400150 | Filter | 1 | 1 |  |
| 201A-13 | 81400145 | Socket bolt | 4 | 4 |  |
| 201A-14 | 81400024 | Reservoir | 1 | 1 |  |
| 201A-15 | 420148 | Cup Head Bolt With Washer | 4 | 4 |  |
| 201A-16 | 81400066 | Cover of Capacitor | 2 | 2 |  |
| 201A-17 | 81400130 | Start Capacitor | 1 | 1 |  |
| 201A-17A | 81400088 | Running Capacitor | 1 | 1 |  |
| 201A-18 | 81400180 | Rubber Gasket | 2 | 2 |  |
| 201A-19 | 420148 | Cup Head Bolt With Washer | 2 | 2 |  |
| 201A-20 | 81400050 | Cover of Motor Terminal Box | 1 | 1 |  |
| 201A-21 | 81400045 | Push Button | 1 | 1 |  |
| 201A-22 | 81400044 | Check Valve | 1 | 1 |  |
| 201A-23 | 81400075 | Release Valve | 1 | 1 |  |
| 201A-24 | 81400117 | Handle For Release Valve | 1 | 1 |  |
| 201A-25 | 81400181 | Washer | 1 | 1 |  |
| 201A-26 | 81400182 | Hex Nut | 1 | 1 |  |
| 201A-27 | 81400041 | Gear Pump | 1 | 1 |  |
| 201A-28 | 81400084 | Oil Return Pipe | 1 | 1 |  |
| 201A-29 | 81400113 | Filler Cap | 1 | 1 |  |

| Item | Part# | Description | Qty. | Note |
| --- | --- | --- | --- | --- |
|  |  |  | 209C | 209CH |  |
| Parts For PEAK Manual Power Unit 380V/50Hz/3 phase (See Fig. 45) |
| 201B-1 | 81400183 | Motor | 1 | 1 |  |
| 201B-2 | 81400178 | Protective Ring | 1 | 1 |  |
| 201B-3 | 81400184 | AC contactor | 1 | 1 |  |
| 201B-4 | 81400127 | Motor Connecting Shaft | 1 | 1 |  |
| 201B-5 | 81400177 | Valve Body | 1 | 1 |  |
| 201B-6 | 81400175 | Relief Valve | 1 | 1 |  |
| 201B-7 | 81400107 | Throttle valve | 1 | 1 |  |
| 201B-8 | 209149 | Lock Washer | 4 | 4 |  |
| 201B-9 | 81400148 | Socket Bolt | 4 | 4 |  |
| 201B-10 | 81400134 | Inlet Pipe | 1 | 1 |  |
| 201B-11 | 81400144 | O-Ring | 1 | 1 |  |
| 201B-12 | 81400150 | Filter | 1 | 1 |  |
| 201B-13 | 81400145 | Socket bolt | 4 | 4 |  |
| 201B-14 | 81400024 | Reservoir | 1 | 1 |  |
| 201B-15 | 420148 | Cup Head Bolt With Washer | 2 | 2 |  |
| 201B-16 | 81400050 | Cover of Motor Terminal Box | 1 | 1 |  |
| 201B-17 | 81400045 | Push Button | 1 | 1 |  |
| 201B-18 | 81400044 | Check Valve | 1 | 1 |  |
| 201B-19 | 81400075 | Release Valve | 1 | 1 |  |
| 201B-20 | 81400117 | Handle For Release Valve | 1 | 1 |  |
| 201B-21 | 81400181 | Washer | 1 | 1 |  |
| 201B-22 | 81400182 | Hex Nut | 1 | 1 |  |
| 201B-23 | 81400041 | Gear Pump | 1 | 1 |  |
| 201B-24 | 81400084 | Oil Return Pipe | 1 | 1 |  |
| 201B-25 | 81400113 | Filler Cap | 1 | 1 |  |

# Text boxes

Fig. 1

1343mm

950mm

2528mm

722mm

1285mm

Fig. 2

Concrete must be 3,000psi (210kg/cm²) minimum

82

Fig. 4

Model 209C 209CH

Fig. 5

Click a line

Fig. 6

Aluminum Name plate

Parts box

Top Connecting Assy.

Lifting Arm

Extension Column

（Outer Column）

Shipment Parts list

Fig. 7

Fig. 9

Parts in the parts box (96)

Fig. 8

Parts in the shipment parts list

96

209C/209CH

Fig. 10

209C/209CH

Fig. 11

Fig. 12

44

44

Fig. 14 High Setting

Fig. 13 Low Setting

6

Width between Columns: 2850mm

78

82

84A/84B

Overall width：3428mm

Note: Minimum embedment of anchors is 90mm.

90mm

Cleaning

Drilling

Bolting

Fig. 15

Fig. 16

Tighten the anchor bolts with ratchet spanner with socket

Note: Torque of Anchors is 150N.m.

Fig. 17

Loosen screw of drive rod for adjustment, tighten the screw after adjustment

Adjust drive rod of limit switch

Limit switch connected with cable

Connect the brown wire to the terminal 12# on limit switch and terminal 4# on control button.

Connect the blue wire to terminal 11# on limit switch and terminal A1 on AC contactor of power unit

Connect the yellow and green wire to the earth wire terminal on limit switch and the earth wire terminal of power unit.

Fig. 18

NC: Normal contact

Bending here

Fig. 19  Powerside Safety Device

Fig. 20  Offside Safety Device

Fig. 21

Low Setting

Cable2

Cable1

84

Cable2

85

Fig. 22

High Setting

Screw the two cable nuts

Cable Connecting direction

Cable connecting direction

Fig. 23

Cable 2

Cable 1

84

85

Cable 2

Fig. 24

Retainer

95

Oil Hose for Cylinder

Oil Hose for Power unit

Fig. 25

View A

Tighten Nut after finishing  installation of safety cable

View B

Assemble Safety Cable from Offside Safety Assy.

Fig. 26

Safety Cable

Oil Hose

Wire Cable

Offside Safety Device

Fig. 28

Powerside Safety Device

Fig. 27

Extension column

Install with cup head bolt

Safety cable

Oil hose

protective cover

Wire cable

Inner column

After install the wire protective cover

Fig. 30

Before install the wire protective cover

Fig. 29

The safety cable cannot put inside cable clamp on top of overhead beam

Oil hose

Wire cable for limit switch

Fig. 31

Loosen the Bolt

Use the 8# Socket Head Wrench to loosen the Socket Bolt

Fig. 33

Snap Ring

Fig. 32

Moon Gear

Locking the bolts after the moon gear and arm lock engaged well

Locking the bolt

Fig. 34

Fig. 35

AC contactor

Fig. 36

N

Motor Line

3#

L

11#

12#

4#

L1

3#

A1

4#

Remove this wire before connecting the Limit Switch

Fig. 38

Fig. 37

L

G

Earth wire

N

Earth Wire

Fig. 39

Three phase

Fig. 40

Fig. 41

Vehicle drive in Direction

Fig. 42

Fig. 44

380V/50HZ/3 phase

220V/50HZ/1 phase

Fig. 45

Relief valve

Capacitor

Oil return port

Protective ring

Check valve

Auxiliary hole

Auxiliary hole

Release valve

Oil Outlet

Handle for Release valve

Fig. 46

Running capacitor

Protective ring

Start capacitor

Relief valve

Check valve

Oil return port

Throttle valve

Release valve

Oil Outlet

Handle for Release valve

Fig. 47

Protective ring

Relief valve

Oil return port

Check valve

Throttle valve

Release valve

Handle of release valve

Oil outlet

Fig. 48

Cable nut

Fig. 49

Bleeding plug

Fig. 50

Counterclockwise to increase the  down speed

Clockwise to decrease the  down speed

Throttle Valve

Fixing Nut

Fig. 51

72220603

11/2015